## Slide 1: CONCEPT AND CONDUCT OF CRASH INVESTIGATION

## Slide 2: INTRODUCTION
Crash investigation is an important element in the entire incident management process at a crash scene. It is an effort to determine how the crash occurred. Investigation is required to document the cause and description of traffic crashes.

## Slide 3: INTRO CONTD
Information that is collected during a crash investigation which is similar, can be used by traffic engineers to support safety improvement in crash prone areas. The information may also be used by insurance companies to provide information for litigation purpose.

## Slide 4: INTRO CONTD
After a crash has occurred, law enforcement officers(Police, FRSC and VIO)with their unique report form are required to complete a crash report form. The purpose of this procedure is to collect information regarding the nature and cause of crash,thus the Concept and Conduct of Crash Investigation.

## Slide 5: AIM
The aim of this lecture is to introduce the course participants to The Elements and procedure of Road Crash Investigation.

## Slide 6: OBJECTIVES
At the end of this lecture, the participants are expected to be able to explain the following;
What Road crash investigation is
Elements of Road crash
procedures of Road crash investigation

## Slide 7: WHAT IS ROAD CRASH INVESTIGATION?
Crash- Collide violently with an obstacle or another vehicle.
Investigate- Carryout a systematic or formal inquiry into (an incident or allegation) so as to establish the truth. (Concise Oxford Dictionary).
Crash Investigation can be defined as a procedure in carrying out a systematic inquiry into vehicle collision with an obstacle or another vehicle, so as to establish the truth.

## Slide 8: ELEMENTS OF ROAD CRASH INVESTIGATION
In crash investigation, crash reporting is the first level. The FRSC staff report officially events surrounding a crash. The accuracy and completeness of the report will depends on the quality of an officer investigating and his attention to details.

## Slide 9: ELEMENTS OF ROAD CRASH INVESTIGATION CONTD
However, there are five types of evidences from the roadway;
1.Final resting positions of made by a tire that is locked and is not free to rotate vehicles and bodies, which could be controlled that is final resting position as done by the driver and uncontrolled as propelled by law of physics.
2.Tire Marks that consist of three categories namely (i)skids made by a tire that is locked and is not free to rotate, which can be skip, gap or curved skids with following evidences

## Slide 10: ELEMENTS OF ROAD CRASH INVESTIGATION CONTD
-The location and direction of travel for the vehicle.
-The drivers’ intention to slow or stop.
-Provides possible evidence as to the speed of the vehicle.
-Helps define area of impact by way of offsets in the skid.
(ii)Yaw marks are made by tires freely rotating but also sliding to the side, with the following evidences –
-The vehicle was traveling too fast to negotiate the curve.
-The vehicle's location and direction on the roadway.
-The driver's intention was not to stop but rather to steer.
-Very accurate in determining speed of vehicle.

## Slide 11: ELEMENTS OF ROAD CRASH INVESTIGATION CONTD
(iii)Tire prints are caused by tires rotating in normal fashion and freely. Tire prints are typically seen when a vehicle‘s wheels travel through soft material or fluid (slush, sand, or snow).
As evidence, tire prints can illustrate:
-The location and direction of the vehicle.
-The drivers’ intention was not to brake, and it may indicate that the driver was on steering

## Slide 12: ELEMENTS OF ROAD CRASH INVESTIGATION CONTD
(3)Gouge Marks,although sometimes called by different names, a gouge mark is a physical damage caused to the road when some parts of the vehicle strikes the roadway.
(4) Debris is the most common type of physical evidence found at the scene of a crash. Debris refers to broken parts, dirt, or fluid dislodged from the vehicle during the impact.
(5)Damage to roadside objects: Damaged objects such as trees, mailboxes, ditch culverts, signs, fences, and other structures can help officers understand events that have occurred.

## Slide 13: PROCEDURES OF CRASH INVESTIGATION
In carrying out crash investigation, there are some steps to be taken in order to achieve the desired goal. They are as follows:
Establishing a reference point(s) is a permanent location that officers or someone else can locate at the scene. This point can be a tangible reference point when there is a fixed object or landmark already at the scene like Fire hydrants, Utility poles, Bridges, Building etc. And Intangible reference points are those which the officer places at the scene and must be related to and measured from a tangible reference point. Examples of intangible reference points are: Points at which extended curb lines intersect. It is marked on the roadway with chalk or paint.

## Slide 14: PROCEDURES OF CRASH INVESTIGATION CONTD
2. Measurement: After the reference points (RP) have been determined, officers need to take measurements. Equipment needed to take measurements are:
  Two measuring tapes - one at least 100 feet and one 25 feet. Steel tape is the most accurate because it does not stretch, like fabric or fiberglass tape. However, steel tape will rust once wet.
  Wheel tape. These can be used on smooth surfaces, but make sure that the wheel stays in contact with the ground at all times.

## Slide 15: PROCEDURES OF CRASH INVESTIGATION CONTD
However, There are six methods used to take measurements: The coordinate method which involves taking two measurements(distance and direction) from a reference point and the triangulation method though complex but more preferred, practical and appropriate in absence of good reference point, are common ones. Other methods include Total station survey equipment, Aerial photograph, Laser range finder system, A global positioning system(GPS) based system.

## Slide 16: PROCEDURES OF CRASH INVESTIGATION CONTD
3.Field Sketch being one of the procedural steps to be taken in order to achieve the desired goal in road crash investigation, is an important tool for crash scene investigators. Typically not drawn to scale, but the diagrams that can help officers illustrate evidence and re-create future drawings needed for the Crash Report.
CONCLUSION
Investigating a collision requires more than checking boxes on a form. Officers must recognize, preserve, and collect all relevant evidence. They must also document the event thoroughly, possibly for others not present, so they can fully understand what happened.
The investigation of traffic collisions is one of the most common in law enforcement activity. Many times it involves the least serious crimes, with the most serious consequences. The dedication and commitment exercised by the investigator could mean the difference between an investigation and a report.